## Slide 1: Chapter 2 01 Polynomial System
How to Use MATLAB/SIMULINK
Created: 14 September 2026
Updated: 16 September 2026
By Nathaniel Tyler

## Slide 2: Git Hub Training Repo
How to Download the Git Repo
Git Hub Webpage
  ntylerbelcan/aviation-controls-simulink-training-Belcan
Ensure you are in a folder called “GitHub” before your run either of the following commands:
  In Git Bash / Terminal you can run
    git clone https://github.com/ntylerbelcan/aviation-controls-simulink-training-Belcan.git
  OR
  In MATLAB
    You can clone directly from the MATLAB command window:MATLAB
    system('git clone https://github.com/ntylerbelcan/aviation-controls-simulink-training-Belcan.git')

## Slide 3: Success looks like knowing how to …
What does success look like?
Create a new Simulink Model from equation
Use blocks
Use Property inspector
Run a simulation
Use Data inspector
Use Model Explorer
Shows a final product of the Example we will be walking thru:
  Slide 3: Final Thought Process (shows the thought process I used to get to the Simulink model)
  Slide 4: Final Simulink Model
  Slide 5: Final Data Dictionary
  Slide 6: Final Model Configuration
  Slide 7: Final Data Inspector

## Slide 4: Final Model (This summarizes all work created thru the powerpoint)

## Slide 5: Original Equation I see , and I mentally decompose it into terms that become blocks. What's going on in my head after I see original equation: Step 1. Original Equation Step 2. Rearrange the polynomial Step 3. Add Parenthesis Step 4. Step 5. COEFF_A = 1 COEFF_B = -4 COEFF_C = 21 Model Construction Logic: Step 1: Calculate t² Step 2: Calculate -4t Step 3: Apply Constant Term (21) Step 4: Sum All Terms Step 5: Output y See next page for final Simulink model. See Slide 11 – 17 for more details
Converting an Equation into a Simulink Model
Important:
Gain Block = Multiplication Output = Input × Gain

## Slide 6: polynomial_System.slx (Model File) Note: How your Model Should look when Finished
Final Setup

## Slide 7: polynomial_System.sldd (Data Dictionary) Note: Contains Signals & Parameters Note: Contains Signals & Parameters
Final Setup
Name | Value | EntryType | DataType | Dimensions | Min | Max | Unit | Description
y_raw |  | Simulink.Signal | double | 1 | 17 | 186 |  | Intermediate polynomial result
y |  | Simulink.Signal | double | 1 | 17 | 186 |  | Polynomial output
t_squared |  | Simulink.Signal | double | 1 | 0 | 225 |  | Square of time
t |  | Simulink.Signal | double | 1 | 0 | 15 | s | 
neg_4t |  | Simulink.Signal | double | 1 | -60 | 0 |  | -4 multiplied by time
coeffA_t_squared |  | Simulink.Signal | double | 1 | 0 | 225 | s^2 | Coefficient A multiplied by the squared time term.
COEFF_C | 21 | Simulink.Parameter | double | [1 1] |  |  |  | Constant offset applied to the polynomial equation.
COEFF_B | -4 | Simulink.Parameter | double | [1 1] |  |  |  | Coefficient applied to the time term.
COEFF_A | 1 | Simulink.Parameter | double | [1 1] |  |  |  | Coefficient applied to the squared time term.

## Slide 8: polynomial_System.slx (Model Settings) Note: How you Models Settings should be setup.
Final Setup

## Slide 9: Data Inspector
Final Setup

## Slide 10: How Engineers Think About Equations

## Slide 11: How Engineers Think About Equations
Important
Do not ask: "How do I build this model?“
Ask: "What mathematical operations make up this equation?“
This same process applies to:
Algebraic Equations Polynomial Equations Differential Equations
State Space Models Control Systems
How Engineers Think About Equations
Key Concept
Simulink models are graphical representations of mathematical operations. Engineers do not build the entire equation at once. They decompose it into smaller operations that can be implemented as blocks.
Example
Identify Terms:
These terms will become the individual signal paths and mathematical operations used to construct the Simulink model shown on the next slide.
Equation
↓
Identify Terms
↓
Identify Operations
↓
Determine Data Flow
↓
Assign Simulink Blocks
↓
Connect Signals
↓
Generate Output
Mathematics Simulink Block
Addition (+) Sum
Subtraction (-) Sum
Multiplication (*) Gain / Product
Constant Value Constant
Power (t²) Math Function
Output (y) Outport

## Slide 12: Equation Decomposition
ENGINEERING RULE
Do not model the equation.
Model the mathematical operations that make up this equation.
How Engineers Think About Equations
Original Equation
Step 1: Split into Terms
Step 2: Identify Operations
 Power
 Multiplication
 Constant
Assign Simulink Blocks
Each operation is implemented by one or more Simulink blocks.
Equation
↓
Identify Terms
↓
Identify Operations
↓
Determine Data Flow
↓
Assign Simulink Blocks
↓
Connect Signals
↓
Generate Output
Mathematical Term Simulink Block
Math Function
Gain Block
Constant Block
Addition Sum Block
Output y Outport

## Slide 13: From Mathematical Operations to Signal Flow
IMPORTANT
Before selecting blocks, understand how information must flow through the model. Signals represent data moving between mathematical operations.
How Engineers Think About Equations
The goal is to understand how information (signals) moves through the model before selecting Simulink blocks.
Starting Variable
t
↓
------+------
↓ ↓
↓ ↓
------+------
↓
+
↓
Signal Paths
Path 1: 
Path 2: 
Path 3: Constant
Final Step:
Combine all three terms to produce y.

## Slide 14: Implementing Signal Flow Using Simulink Blocks
Mathematical Operation → Simulink Block
Signal Flow
t
↓
------+------
↓ ↓
↓ ↓
------+------
↓
+
↓
How Engineers Think About Equations
Power (t²) → Math Function
Multiplication (-4t) → Gain
Constant (21) → Constant
Addition → Sum
Output (y) → Outport
Implementation Concept
Clock
↓
+ → Math Function → +
↓ ↓
+ → Gain (-4) → → →+ → Sum → y
↓ ↑
+ → Constant (21) → +
IMPORTANT
The mathematics has not changed. We are replacing each mathematical operation with a corresponding Simulink block.

## Slide 15: Original Equation I see , and I mentally decompose it into terms that become blocks. What's going on in my head after I see original equation: Step 1. Original Equation Step 2. Rearrange the polynomial Step 3. Add Parenthesis Step 4. Step 5. COEFF_A = 1 COEFF_B = -4 COEFF_C = 21 Model Construction Logic: Step 1: Calculate t² Step 2: Calculate -4t Step 3: Apply Constant Term (21) Step 4: Sum All Terms Step 5: Output y See next page for final Simulink model.
Converting an Equation into a Simulink Model
Important:
Gain Block = Multiplication Output = Input × Gain

## Slide 16: The model implements: y = t² - 4t + 21 (THIS IS THE FINAL IMPLIMENTATION)
Final Simulink Implementation

## Slide 17: How to Open MATLAB & SIMULINK

## Slide 18: Open MATLAB
How to Open MATLAB & SIMULINK

## Slide 19: Review the MATLAB Window Layout
How to Open MATLAB & SIMULINK

## Slide 20: Navigate to training folder (Summary)
Step 2. Navigate to Chapter 2 folder
Step 1. Navigate to training folder
How to Open MATLAB & SIMULINK
Step 2. Navigate to sub folder “02_derivative_System”
Step 1. Double Click

## Slide 21: How to Add To Project

## Slide 22: Add “ch02” Folder and Sub Folders to Project
Step 2. Click “Add Selected Folders and Subfolders”
Step 1. Right Click Folder
How to Add To Project
Step 3. Observe Folder has been added to path

## Slide 23: Create New Folder “02_derivative_System”
Step 1. Double Click ch02 Folder
How to Add To Project
Step 2. Right Click on Empty Space and Click “Folder”
Step 3.
Rename Folder
Step 4. Rename Folder to
02_derivative_System

## Slide 24: Add “02_derivative_System” Folder and Sub Folders to Project
Step 2. Add Selected Folders and Subfolders
Step 1. Right Click Folder
How to Add To Project
Step 3. Observe Folder has been added to path
Step 1. Right Click
Step 1. Observe folder has been added to path

## Slide 25: Navigate to training folder “02_derivative_System”
Step 2. Observe Empty Folder
Step 1. Double Click Folder
How to Add To Project

## Slide 26: How to Create a new Simulink Model

## Slide 27: Detailed Success in this section looks like knowing how to …
How to Create a new Simulink Model
Create a new Simulink Model
  Creating File (slx) Create / Rename / Open

## Slide 28: Navigate to training folder & create Simulink Model
How to Create a new Simulink Model

## Slide 29: Navigate to training folder & create Simulink Model
How to Create a new Simulink Model
1) Click Create Model

## Slide 30: Rename Simulink File
Step 2. Save As “polynomial_System”
Step 1. Click Save
How to Create a new Simulink Model

## Slide 31: Observe File has been Renamed
How to Create a new Simulink Model

## Slide 32: How to Use blocks

## Slide 33: Detailed Success in this section looks like knowing how to …
How to Use blocks (Part 1)
Use blocks
  Blocks Add / Edit / Label
  Model Fit Contents to Window
  Lines Create / Edit / Format / Label / Data log / Resolve
  Signal Attributes View / Edit / Property Inspector

## Slide 34: Add Annotation
Step 2. Type “step” and press enter
Step 1. Double Click on Empty Space
How to Use blocks (Part 1)

## Slide 35: Add Clock
Step 2. Add Clock
Step 1. Double Click empty space
How to Use blocks (Part 1)
Step 3. Rename Clock
1. Click Block
1. Type clo
2. Click

## Slide 36: Added Clock
How to Use blocks (Part 1)

## Slide 37: Add Square
Step 2. Add Square
Step 1. Double Click empty space
How to Use blocks (Part 1)
Step 3. Rename Square
1. Type sq
2. Click
1. Click Block

## Slide 38: Added Square
How to Use blocks (Part 1)

## Slide 39: Add 1st Gain Block
Step 2. Add Gain
Step 1. Double Click empty space
How to Use blocks (Part 1)
Step 3. Rename Gain
2. Click
1. Type gain
1. Click Block

## Slide 40: Added 1st Gain Block
How to Use blocks (Part 1)

## Slide 41: Add 2nd Gain Block
Step 2. Observe Duplication Result
Step 1. Duplicate Gain block by Holding ctrl and Dragging gain block down
How to Use blocks (Part 1)
Step 3. Rename Gain
Step 1. Hold ctrl and drag gain block down
Step 1. Observe New Gain block that was generated
Step 1. Rename Gain Block

## Slide 42: Added 2nd Gain Block
How to Use blocks (Part 1)

## Slide 43: Add Constant Block
Step 2. Add Constant Block
Step 1. Double Click empty space
How to Use blocks (Part 1)
Step 3. Rename Constant Block
1. Type con
2. Click
1. Click Block

## Slide 44: Added Constant Block
How to Use blocks (Part 1)

## Slide 45: Add Sum Block
Step 2. Add Sum Block & Edit Block Parameters
Step 1. Double Click empty space
How to Use blocks (Part 1)
Step 3. Rename and resize Sum Block
Step 1. Double Click Sum
Step 2. Update Icon Shape “rectangular” & list signs “+++”
Step 3. Click Apply
1. Type sum
2. Click

## Slide 46: Added Constant Block
How to Use blocks (Part 1)

## Slide 47: Add Data Type Conversion Block
Step 2. Add Data Type Conversion
Step 1. Double Click empty space
How to Use blocks (Part 1)
Step 3. Rename Data Type Conversion
2. Click
1. Type conve
1. Click Block

## Slide 48: Added Data Type Conversion Block
How to Use blocks (Part 1)

## Slide 49: Add Outport Block
Step 2. Add Outport
Step 1. Double Click empty space
How to Use blocks (Part 1)
Step 3. Rename Outport
1. Type out
2. Click
1. Click Block

## Slide 50: Added Outport Block
How to Use blocks (Part 1)

## Slide 51: Add Signal Lines
How to Use blocks (Part 1)

## Slide 52: Align Blocks
How to Use blocks (Part 1)

## Slide 53: Show Property Inspector (Method 1) Note: This is my preferred method
Step 2. Click Down Arrow and then Click Restore
Step 1. Click Property Inspector
How to Use blocks (Part 1)

## Slide 54: Show Property Inspector (Method 2) Note: This method will force property Inspector to activate
Step 2. Click Property Inspector
Step 1. Click “MODELING” Tab and expand options
How to Use blocks (Part 1)

## Slide 55: Update Signal: t
Step 2. Check Boxes
Step 1. Select Line and Update Signal Name
How to Use blocks (Part 1)
Step 1. Select Line
Step 2. Observe
Step 1. Check Boxes

## Slide 56: Update Signal: t_squared
Step 2. Check Boxes
Step 1. Select Line and Update Signal Name
How to Use blocks (Part 1)
Step 1. Select Line
Step 1. Check Boxes
Step 2. Observe

## Slide 57: Update Parameter: COEFF_A
Step 2. Observe renamed parameter
Step 1. Select Line and Update Parameter Name
How to Use blocks (Part 1)
Step 1. Select Block
Step 1. Check Boxes
Step 2. Observe

## Slide 58: Format Blocks to Same Size Note: The last block you select is used as the formatting reference. All other selected blocks will be formatted to match it.
Step 2. Select Final Block
Step 1. Select Blocks
How to Use blocks (Part 1)
Step 3. Format Blocks
Step 1. Select Blocks
Step 1. Shift Hold Select Block
Step 1. Click Match
Step 2. Observe

## Slide 59: Format Blocks to Same Size Note: The last block you select is used as the formatting reference. All other selected blocks will be formatted to match it.
Step 2. Observe Aligned Blocks
Step 1. Select Blocks
How to Use blocks (Part 1)
Step 1. Select Blocks
Step 2. Shift Hold Select Block
Step 2. Observe
Step 1. Click Align

## Slide 60: Update Parameters: COEFF_B & COEFF_C
Step 2. Update Constant Block
Step 1. Update Gain block
How to Use blocks (Part 1)

## Slide 61: Update Signal: coeffA_t_squared
Step 2. Check Boxes
Step 1. Select Line and Update Signal Name
How to Use blocks (Part 1)
Step 1. Select Line
Step 1. Check Boxes
Step 2. Observe

## Slide 62: Update Signal: neg_4t
Step 2. Check Boxes
Step 1. Select Line and Update Signal Name
How to Use blocks (Part 1)
Step 1. Select Line
Step 1. Check Boxes
Step 2. Observe

## Slide 63: Update Signal: const_21
Step 2. Check Boxes
Step 1. Select Line and Update Signal Name
How to Use blocks (Part 1)
Step 1. Select Line
Step 1. Check Boxes
Step 2. Observe

## Slide 64: Update Signal: y_raw
Step 2. Check Boxes
Step 1. Select Line and Update Signal Name
How to Use blocks (Part 1)
Step 1. Select Line
Step 1. Check Boxes
Step 2. Observe

## Slide 65: Update Signal: y
Step 2. Check Boxes
Step 1. Select Line and Update Signal Name
How to Use blocks (Part 1)
Step 1. Select Line
Step 1. Check Boxes
Step 2. Observe

## Slide 66: Save Model File
Step 2. Observe the Saved File
Step 1. Click Save (* indicates the file is unsaved)
Note: ctrl + s will also save the document
How to Use blocks (Part 1)

## Slide 67: How to Use Model Configuration

## Slide 68: Detailed Success in this section looks like knowing how to …
How to Use Model Configurations
Use blocks
  Model Settings Edit

## Slide 69: Update Model Configurations (Part 1)
Step 2. Observe the opened Model Configuration.
Step 1. Click Model Settings
How to Use Model Configurations

## Slide 70: Update Model Configurations (Part 2)
Step 2. Observe Stop time after clicking apply
Step 1 Update Model Configuration Settings
How to Use Model Configurations
Step 2. Set Type to Fixed-step
Step 1. Set Type to 15
Step 3. Set Solver to discrete
Step 4. Set Fixed-step size to 0.25
Step 5. Click Apply
Step 1. Observe Stop Time was Updated

## Slide 71: Save Model File
Step 2. Observe the Saved File
Step 1. Click Save (* indicates the file is unsaved)
Note: ctrl + s will also save the document
How to Use Model Configurations

## Slide 72: How to Use Model Explorer

## Slide 73: Detailed Success in this section looks like knowing how to …
How to Use Model Explorer
Use Model Explorer
  Data Dictionary (sldd) Create / Edit

## Slide 74: Open Model Explorer
Step 2. Observe Model Explorer Window
Step 1. Click “MODELING” Tab and Click “Model Explorer”
How to Use Model Explorer
Step 1. Click “MODELING” Tab
Step 2. Click “Model Explorer”

## Slide 75: Create Data Dictionary File (.sldd)
Step 1. Drill Down to “External Data” and then Click “New”
How to Use Model Explorer
Step 1. Drill Down to “External Data”
Step 2. Click New to create a new data dictionary

## Slide 76: Create Data Dictionary File (.sldd)
Step 2) Apply Changes
Step 1. Save file as “polynomial_System”
How to Use Model Explorer
Step 1. Create File polynomial_System.sldd
Step 2. Click Save
Step 1. Observe our created file polynomial_System.sldd
This will hold our signal definitions and more .
Step 2. Click Apply

## Slide 77: Open Design Data
Step 2. Drill down to Design Data
Step 1. Click “polynomial_System”
How to Use Model Explorer
Step 3. Observe Design Data
Step 1. Click
Step 1. Expand
Step 2. Click

## Slide 78: Add Simulink Signal Note: Just Create the blank signal for now
Step 1. Click “Simulink Signal” x6
Note: This will add a new signal to your data inspector.
How to Use Model Explorer
Step 1. Click “Simulink Signal”
Repeat Action x6

## Slide 79: Add Simulink Parameter Note: Just Create the blank parameter for now
Step 1. Click “Simulink Parameter”
Repeat Action x3
Step 1. Click “Simulink Parameter” x3
Note: This will add a new signal to your data inspector.
How to Use Model Explorer

## Slide 80: Rename Signals and Parameters
Step 1. Update Names
Step 1. Click each row and update the Name of each signal and parameter Note: This will add a new signal to your data inspector.
How to Use Model Explorer
Step 2. Observe Columns prior to Update (Next 3 slides will update these columns)

## Slide 81: Mass Update Data Type Note: Mandatory
Step 2. Click & Update Field
Step 1. Shift + Hold + select rows
How to Use Model Explorer
Step 3. Observe updated column
Step 1. Observe Data Type Before Update is “auto”
Step 1. Observe Data Type After Update is “double”
1. Click field
2. Select

## Slide 82: Mass Update Dimensions Note: Optional
Step 2. Click & Update Field
Step 1. Shift + Hold + select rows
How to Use Model Explorer
Step 3. Observe updated column
Step 1. Observe Dimensions Before Update is -1 or [0 0]
Step 1. Observe Dimensions After Update is 1 or [1 1]
Step 1. Click field
Step 2. Type 1

## Slide 83: Mass Update Storage Class Note: Optional
Step 2. Click & Update Field
Step 1. Shift + Hold + select rows
How to Use Model Explorer
Step 3. Observe updated column
Step 1. Observe Storage Class Before Update is auto
Step 1. Observe Storage Class After Update is ExportedGlobal
1. Click field
2. Select

## Slide 84: Observe Data Dictionary After Mass Update
Step 1. Observe Updated Columns
How to Use Model Explorer
Step 1. Observe Updated Columns

## Slide 85: Update Signal: y_raw
Step 1. Select Signal and Update remaining fields
How to Use Model Explorer
Step 2. Update Min, Max, & Description
Step 1. Select signal

## Slide 86: Update Signal: y
Step 1. Select Signal and Update remaining fields
How to Use Model Explorer
Step 2. Update Min, Max, & Description
Step 1. Select signal

## Slide 87: Update Signal: t_squared
Step 1. Select Signal and Update remaining fields
How to Use Model Explorer
Step 2. Update Min, Max, & Description
Step 1. Select signal

## Slide 88: Update Signal: t
Step 1. Select Signal and Update remaining fields
How to Use Model Explorer
Step 1. Select signal
Step 2. Click & Update fields Min, Max, & Unit

## Slide 89: Update Signal: neg_4t
Step 1. Select Signal and Update remaining fields
How to Use Model Explorer
Step 3. Update Description
Step 1. Select signal
Step 2. Click & Update fields Min & Max

## Slide 90: Update Signal: coeffA_t_squared
Step 1. Select Signal and Update remaining fields
How to Use Model Explorer
Step 3. Update Description
Step 1. Select signal
Step 2. Click & Update fields Min, Max, & Unit

## Slide 91: Update Parameter: COEFF_C
Step 1. Select Signal and Update remaining fields
How to Use Model Explorer
Step 3. Update Description
Step 1. Select Param
Step 2. Update Value

## Slide 92: Update Parameter: COEFF_B
Step 1. Select Signal and Update remaining fields
How to Use Model Explorer
Step 3. Update Description
Step 1. Select Param
Step 2. Update Value

## Slide 93: Update Parameter: COEFF_A
Step 1. Select Signal and Update remaining fields
How to Use Model Explorer
Step 3. Update Description
Step 1. Select Param
Step 2. Update Value

## Slide 94: Save Changes made to Data Dictionary (.sldd) Note: Changes made to the data dictionary must be saved from Model Explorer. Otherwise, the changes will not be applied and may be lost. Note: Pressing Ctrl+S in Model Explorer does not save data dictionary changes. Instead, it may create a new signal or have a different action than expected. To save dictionary changes, right-click the data dictionary and select Save Changes. Yes, this behavior surprises everyone at least once.
Step 2. Right Click & Save Changes
Step 1. Click polynomial_System*
How to Use Model Explorer
Step 3. Observe Saved File
1. Click
1. Right Click
2. Click Save

## Slide 95: Save Model File
Step 2. Observe the Saved File
Step 1. Click Save (* indicates the file is unsaved)
Note: ctrl + s will also save the document
How to Use Model Configurations

## Slide 96: How to Run a simulation

## Slide 97: Detailed Success in this section looks like knowing how to …
How to Run a simulation
Run a simulation
  Run Shortcut (CTRL+T)
  Stop Time Value is 15 sec

## Slide 98: Run Simulation
Step 1. Click Run or press CTRL+T
How to Run a simulation
2. Click Run or press CTRL+T
1. Click Tab “SIMULATION”

## Slide 99: How to Use Data inspector

## Slide 100: Detailed Success in this section looks like knowing how to …
How to Use Data inspector
Use Data inspector
  Graph Graph Data / Edit Grid / Use Cursors
  Stop Time Value is 15 sec

## Slide 101: Open Data Inspector Note: Simulation must be run prior to opening Data inspector to observe raw values.
Step 1. Click Data Inspector
How to Use Data inspector
2. Click Data Inspector
1. Click Tab “SIMULATION”

## Slide 102: Setup Data Inspector
How to Use Data inspector

## Slide 103: Add Cursor
How to Use Data inspector

## Slide 104: Save Data Inspector File
Click Save / Save As
Click Save Icon
How to Use Data inspector
Save File

## Slide 105
▶ Launch Quiz

## Slide 106: Relaunch the add-in
Microsoft Power BI
Return to your internet browser or copy this link into your browser:
https://pages.store.office.com/addinsinstallpage.aspx?rs=en-US&assetid=WA200003233&isWac=True&ui=en-US&ad=US
Need more help?
Add-ins
Home
On the Home tab
After you install the add-in, you can launch it by choosing the add-in button on the Home tab

## Slide 107
Microsoft Power BI Test Results

## Slide 108: Admin Only Links
Quiz – Summary Page METRICS for Mike and Brandon
Quiz – Responses Overview
Quiz – Excel Log
My files – OneDrive Where Excel Log is stored
Power BI – Workspace My workspace
Power BI – Semantic Model Training Quiz Results Master Power Queries
Power BI – Results Training Performance Dashboard Power BI Dashboard
Only the Admin uses these links